## Slide 1
REASON:
Be informed that with the aim to improve our equipment,
MODIFICATIONS:
The following modifications have been made to the Z4000 JDE coffee group:
the restrictor diameter of ES nozzle assembly has been reduced from 0,7 mm to 0,6 mm
Coffee filter Ø42 mm for upper piston has been replaced by coffee microfilter Ø42 mm
Modified
ES nozzle assembly
Upper piston
Coffee microfilter Ø42 mm
Restrictor diameter
0,6 mm (it was 0,7)
Modified
Z4000 JDE coffee group
Revision 02
1
2

## Slide 2
Machines concerned by modification from S/N 34920075.
EXCHANGEABILITY:
Modified parts or assemblies can be used on machines produced before S/N above.
Pre – modification codes will be available while stocks last.
Modified ES nozzle assembly
(Restrictor diameter 0,6 mm)
Spare part code: 266424
Pre-modification ES nozzle assembly
(Restrictor diameter 0,7 mm)
Spare part code: 261863
Coffee microfilter Ø42 mm
Spare part code: 265809
Pre-modification coffe filter Ø42 mm
Spare part code: 261755
Modified Z4000 JDE coffee group
Spare part code: 266423
Pre-modification Z4000 JDE coffee group
Spare part code: 261862